## Slide 2: Positive Clamper

## Slide 3
Initial Circuit

## Slide 4
1st Positive Half Cycle
Diode is reverse biased  Open circuit
Capacitor takes 5 times tau (5*tau) to charge to 2/3 percent
Time constant = 10*Time period of input  So capacitor does not even start charging

## Slide 5
1st Negative Half Cycle (till negative peak is reached)
Diode is Forward biased  Short circuit
Since it is short circuit, large current flows and this current charges the capacitor to V_m in shorter duration

## Slide 6
1st Negative Half Cycle (At the point when negative peak is reached)
Capacitor is charged to V_m
It cannot discharge quickly since time constant is very large
Voltage across diode  0V = - Vp + Vp = 0 => No current flows
Diode becomes open circuit. Vo = -Vp + Vp = 0
Now the current flows through load.

## Slide 7
1st Negative Half Cycle (After negative peak is reached)
Capacitor gives a voltage of Vp
Net Voltage across diode and load hereafter  = Vin + Vp
Vp is like DC value so the entire waveform is shifted upwards by a value of Vp
Vin + Vp is always greater than or equal to zero hereafter. Hence Diode is always reverse biased (open circuit)

## Slide 8
Initial Circuit